MUSICA

Music theory in Scala

# Real Intervals and Cents Intervals
musica.math.RealInterval, CentsInterval

A real interval is interpreted as a proportion of two positive, real-valued frequencies (or two lengths). It has two attributes: for frequencies f1 and f2, value = f1 / f2 and cents = 1200 2 log (f1 / f2). A value of 2 maps to 1200 cents, and value 1 to 0 cents. Values smaller then 1 map to negative cents. Values cannot be zero or negative. Two real intervals are equal if their value and their cents are equal.

Musica offers the following algebra for real intervals:

Given real intervals a and b then their sum interval c = a + b is defined as:
c.cents = a.cents + b.cents and consequently: c.value = a.value * b.value
and their subtraction is c = a - b:
c.cents = a.cents - b.cents and consequently: c.value = a.value / b.value

The negation of an interval: c = -a is defined as:
c.cents = -a.cents and consequently: c.value = 1/a.value

Real intervals can be (right) multiplied (and divided) by a Double: c = a * k, d = a / k
c.cents = a.cents * k and consequently: c.value = a.valuek
d.cents = a.cents / k and consequently: d.value =a.value-k

Real intevals can be applied to a frequency f to obtain a new frequency: g = a on f
g = f * a.value

It is possible to normalize a real interval, which obtains the octave-equivalent interval with a value between 1 and 2 and cents between 0 and 1200.
b = a.normalize(): b.cents = a.cents modulo 1200 (for whole values)

The trait RealInterval is implemented principally by the immutable class CentsInterval. By default, operations on a real interval produce objects of the class CentsInterval.

Factory objects and implicit conversion are used to create RealIntervals and CentsIntervals. The (Double) parameter always indicates the size of the interval in cents.

Examples:
 val a = CentsInterval( 200.0 )
 val b = RealInterval( 1100 ) // creates a CentsInterval
val c: RealInterval = 1000.0 // implicit conversion
val y: RealInterval = "1000.0c" // another conversion (mind the "c"!)

val d = (a + b) * 3 - (c / 2.5) + 230.0
println (d.value) // 8.6238...
  println (d.cents) // 3730.0

val e = d.normalize
  println (e.value) // 1.0779...
  println (e.cents) // 130.0

println(d on 1.5) // 12.9357...

println(100 + d) // 3830.0 - implicit conversion to double
# Pure Intervals and Rationals
musica.math.PureInterval, Rational

Pure intervals can be expressed by the proportion of two positive integers: n / m. Musica offers a special algebra for pure intervals that allows exact computations. The class PureInterval implements the trait RealInterval, so pure intervals also have a value and cents. They can be added to or subtracted from any other real interval, but the result will be a cents interval and no exact computations will be possible on the result.
Pure intervals are extensions of the class Rational. It means that at their construction, n and m are divided by their graetest common divider to obtain the numerator (numer) and denominator (denom). The valueof a rational is a double equal to 1.0 * n / m. Two rationals are equal when their numerators and denominators are both equal. The class Rational implements 4 operators:
   [n/m] +/- [k/l] = [(n*l +/- k*m) / m*l] ; [n/m] * [k/l] = [n*k / m*l] ; [n/m] / [k/l] = [n*l / m*k]
For Pure Intervals, the algebra differs from the Rational algebra:
addition: [n / m] + [k / l ] = [ (n * k) / (m * l) ] (is a Rational mutliplication)
subtraction: [ n / m ] – [ k / l ] = [ (n * l) / (m * k) ] (is a Rational division)
negation: - [ n / m ] = [ m / n ]
Pure intervals can be right-multiplied by integers:
[ n / m ] * i = [ ni / mi ] (for i >= 0) = [ mi / ni ] (for i < 0)
observe that [ n / m ] * (-i) = - ( [ n / m ] * i)
If Doubles are used or division is applied, a CentsInterval will be produced.

When a Pure Interval is applied to a Double frequency, the result is a Double:
[ n / m ] on r = n * r / m
If a Pure Interval is applied to an Int or a Rational frequency, the result is a Rational:
[ n / m ] on [ a / b ] = [ n * a / m * b ]
Pure intervals can be normalized: which means that they are divided or multplied by powers of 2 such that the result lies between values 1 and 2.
The factory object PureInterval can be used to produce Pure Intervals. It also contains a set of often used intervals:
    val Prime = PureInterval(1, 1)
    val Octave = PureInterval(2, 1)
    val Fifth = PureInterval(3, 2)
    val Fourth = PureInterval(4, 3)
    val MajorThird = PureInterval(5, 4)
    val MinorThird = PureInterval(6, 5)
    val MajorSeventh = PureInterval(7, 6)
    val MinorSeventh = PureInterval(8, 7)
    val MajorTone = PureInterval(9,8)
    val MinorTone = PureInterval(10,9)
    val SemiTone = PureInterval(16,15)
    val PythagoreanComma = (Fifth * 12) - (Octave * 7)
    val SyntonicComma = (Fifth * 4) - (MajorThird + (Octave * 2))
    val EnharmonicComma = Octave - (MajorThird * 3)

Examples:
Creating a Pure interval:
  val a = PureInterval( 48,36 )
  println(a) // 4/3
  println(a.value) // 1.3333...
  println(a.cents) // 498.04449

Some operations:
val b = (PureInterval.Fifth * 4) - (PureInterval.MajorThird +
(PureInterval.Octave * 2))
  println(b) // 81/80 – the Syntonic Comma

Conversion to CentsInterval when:

val c = PureInterval(23,18)
  println ( c * 1.2 ) // 509.237...c - multiply by double
  println ( c + 230.4) // 654.764...c - adding a cents interval, but:
 println ( 100 + c) // 524.366... - implicit conversion to cents (Double)

  val f = RealInterval(c) // explicit conversion
  println(f) // 424.364...c

 Applying to frequencies:

  println (c on 3) // 23/6
  println (c on Rational(3,2)) // 23/12
  println (c on 1.5) // 1.916666....

It is possibe to use a string to create pure intervals:

  val g: PureInterval = "2/3"
## Just Intonation, Eitz notation
There are three functions provided in the PureInterval factory object to compute Just-intonation intervals, using limit-3, limit-5 and limit-7 just intonation:

  def JILimit7(f3: Int, f5: Int, f7: Int): PureInterval = {
      (Fifth * f3 + MajorThird * f5 + MajorSeventh * f7).normalize }
    def JILimit5(f3: Int, f5: Int): PureInterval = {
     (Fifth * f3 + MajorThird * f5).normalize }
def JILimit3(f3: Int): PureInterval = {
      (Fifth * f3).normalize }

Example:

  val e = PureInterval.JILimit5(4,-1)
println(e) // 81/80 – again the Syntonic comma

It is possible to use Eitz' notation for pure intervals in the Euler/Riemann Tonnetz. Use the same notations as for classic notes (see next chapter); the octave-indication is used for the Eitz-layers.

   println(EitzInterval("C0")) // 1/1
  println(EitzInterval("E-1")) // 5/4 = pure third
  println(EitzInterval("E+1")) // 6561/5120
println(EitzInterval("Bb+1")) // 9/5
println(EitzInterval("F##+4")) // 68630377364883/42949672960000

But cents intervals will be produced in this case.

The Eitz-layers (= number of Syntonic comma's) can also be indicated separately, the octaves in the note string are then used normally:

println(EitzInterval("E", -1)) // 5/4 = pure third
println(EitzInterval("E+1", -1)) // 5/2 = pure third + octave

 Non-integer numbers can be used as well, but, again then cents intervals are produced:

  println(EitzInterval("D", -1/3.0)) // third comma: 196.741..c

# Classic Notes
musica.symbol.ClassicNote

Classic notes are most easily created using the notation: note name, deviation, octaves, in which the note names are 'A' to 'G', the deviation is one ore more '#' for sharps and one or more 'b' for flats. Octaves are indicated with '0' for the central octave (0 is default), +1, +2, etc for higher octaves and -1, -2, etc for lower octaves. Use the factory object ClassicNote:
val n = ClassicNote("C#+1")
val a: ClassicNote = "Abb"

You can use numerical parameters as well. Use step, deviation and octave. The default for step and octave is 0. Beware that the step starts with 0 for "C" and only values 0 to 6 are allowed. Deviation and octave can be any integer:

 println( ClassicNote(2,-1,1) ) // Eb+1

You can use fields step, dev and octave to retrieve the properties of a note.

println( "" + n + " "+ n.step +" "+ n.dev+ " " + n.octave ) // C#+1 0 1 1

The chromatic (12-scale) value of a note is indicated by the field chr and the corresponding midi pitch code with the field midicode:

println( "" + a + " " + a.chr + " " + a.midicode) // Abb 7 67

Two notes are called enharmonic if their chromatic value is equal:

    println( a.isEnharmonic("G")) // true

    println( a == "G") // false

(Observe that implicit conversion from String to ClassicNote is applied.)

Classic notes can be normalized, which means setting the octave to 0.

 println( n.normalize ) // C#

Classic notes can also be created by using the Circle of Fifths. At position 0 is the "C". All notes produced this way are normalized.

println (ClassicNote.FifthCircle(2)) // D
println (ClassicNote.FifthCircle(-13)) // Gbb

You can also retrieve the position on the Circle of Fifth for a given classic note (ignoring the octave), using fifth:

println( a.fifth ) // -11

# Classic Intervals
musica.symbol.ClassicInterval

Classic intervals can be created using the standard notation: "P" for pure, "M" for major, "m" for minor, "A" and "d" for augmented and diminished, followed by the number of steps (1 is unison):
val s = ClassicInterval("P5") // pure fifth
val t: ClassicInterval = "m16" // minor sixteenth

In musica there are some additions to this notation. You can indicate an interval downwards by adding a minus sign.
val u: ClassicInterval = "-A4" // augmented fourth down
Intervals with larger deviations are called "irregular" and can be created using "i()" and "I()" and a number indicating the size of the deviation. This number should be positive. "i" is used for intervals smaller than standard, "I" for intervals larger than standard.
val v: ClassicInterval = "i(12)4"
val w: ClassicInterval = "I(10)7"

It is possible to create Classic Intervals using numeric parameters as well. Use parameters step and deviation. Both parameters can be any integer. Step 0 is the unison interval. Negative values for step indicate an interval downwards. The meaning of the deviation differs for intervals that can or cannot be pure. For pure intervals, 0 means pure, -1 means diminished and +1 is augmented. All other values are irregular. For non-pure intervals, 0 means major, -1 minor, -2 diminished and +1 augmented, and all other values irregular.

println(ClassicInterval(0)) // P1
 println(ClassicInterval(2,-1)) // m3
println(ClassicInterval(7,5)) // I(5)8

You can retrieve the step and deviation using fields step and dev:
 println( "" + s + " "+ s.step +" "+ s.dev ) // P5 4 0
It is possible to retrieve the size of the interval (chromatic distance) and the number of complete octaves encompassed:
println( "" + t + " "+ t.size +" "+ t.octaves ) // m16 25 2
Use the function name to get a longer description:
println(t.name) // Minor Second 16va
Intervals are called equal if their step and deviation are equal. They are called enharmonic if they have the same size.
println(ClassicInterval("M2") isEnharmonic "d3") // true
 println(ClassicInterval("M2") == "d3") // false

Classic Intervals can be created from two notes (implicit String conversion):
println(ClassicInterval("C", "E")) // M3
println(ClassicInterval("F+1", "C")) //-P11

A number of classic intervals have been predefined in the factory object ClassicInterval:
def Prime = ClassicInterval(0)
def MinorSecond = ClassicInterval(1,-1)
def MajorSecond = ClassicInterval(1)
def MinorThird = ClassicInterval(2,-1)
def MajorThird = ClassicInterval(2)
def Fourth = ClassicInterval(3)
def Fifth = ClassicInterval(4)
def MinorSixth = ClassicInterval(5,-1)
def MajorSixth = ClassicInterval(5)
def MinorSeventh = ClassicInterval(6,-1)
def MajorSeventh = ClassicInterval(6)
def Octave = ClassicInterval(7)

Classic intervals can be normalized, bringing them back within one octave:

println(t.normalize.name) // Minor Second
 println(u.normalize.name) // Diminished Fifth

Some operations involving classic intervals and notes have been defined. Classic Intervals can be negated, added, subtracted and multiplied by integers:

println( s + t - u*2 ) // A26
println( -s )// -P5

Intervals can be applied on notes, to produce notes:

println (s on "C#") // G#
 println (t below "Ab+2") // G

The inverse of an interval is computed on the normalized version:

println (s invert) // P4
 println (t invert) // M7

# Classic Scales
musica.symbol.ClassicScale

A classic scale is simply a list of classic intervals, in increasing order. There are two ways to define a scale: by providing (a List of) ClassicIntervals, or by simply providing a String with comma-separated interval names (no whitespace). Scales can be applied to a note to create a list of notes:
val scale1 = ClassicScale("P1,M2,M3,P4,P5,M6,M7")
val scale2 = ClassicScale("P1","M2","M3","P4","P5","M6","M7")
 val l: List[ClassicInterval] = List("P1","M2","M3","P4","P5","M6","M7")
val scale3 = ClassicScale(l)
println ( scale1 on "C#" ) // List(C#, D#, E#, F#, G#, A#, B#)

Function step can be used to retrieve the individual intervals on the infinite scale. Step(0) is equal to the firstt interval in the list (most often P1).
 println(scale.step(-4)) // -P5
println(scale.step(-4) on "Ab") // Db

for (i <- -4 to 1) {
        println( ""+i+": "+(scale.step(i)) +" "+(scale.step(i) on "Ab"))
  }
        // -4: -P5 Db
        // -3: -P4 Eb
        // -2: -m3 F
        // -1: -m2 G
        // 0: P1 Ab
        // 1: M2 Bb

Of course, pentatonic or whole-note scales are possible too:

 val pentatonic = ClassicScale("P1,M2,P4,P5,M6")
val wholenote = ClassicScale("P1,M2,M3,A4,A5,A6")
 println ( pentatonic on "F" ) // List(F, G, Bb, C+1, D+1)
println ( wholenote on "C" ) // List(C, D, E, F#, G#, A#)

A few scales have been predefined in the factory object ClassicScale:

println (ClassicScale.Major on "C") // List(C, D, E, F, G, A, B)
println (ClassicScale.Minor on "C") // List(C, D, Eb, F, G, Ab, Bb)
 println (ClassicScale.HarmonicMinor on "C") // List(C, D, Eb, F, G, Ab, B)
 println (ClassicScale.MelodicMinor on "C") // List(C, D, Eb, F, G, A, B)

# Tuning
Musica.math.Tuning

A tuning is basically a list of RealIntervals. They can be created very similar to scales in the previous chapter, by using a list of intervals, a list of strings, or one comma separated string or a List object containing real intervals.
      val eq = Tuning("0c,100c,200c,300c,400c,500c,600c,700c,800c,900c,1000c,1100c")
      val agricola = Tuning("135/128,9/8,1215/1024,81/64,4/3,45/32,	3/2,405/256,27/16,16/9,243/128")
      val werckmeister3 = Tuning("C0,C#-1,D-1/2,Eb0,E-3/4,F0,G-1/4,G#-1,
A-3/4,Bb0,B-3/4")